## Slide 1: Earthquake Analysis of Linear MDoF System
Pertemuan – 11
Mata Kuliah : Dinamika Struktur & Pengantar Rekayasa Kegempaan
Kode : CIV - 308
SKS : 3 SKS

## Slide 2
TIU :
Mahasiswa dapat menjelaskan fenomena-fenomena dinamik secara fisik.
Mahasiswa dapat membuat model matematik dari masalah teknis yang ada serta mencari solusinya
TIK :
Mahasiswa dapat menghitung respon struktur MDoF akibat beban gempa bumi

## Slide 3
Sub Pokok Bahasan :
Persamaan Gerak Sistem MDoF Akibat Beban Gempa Bumi
Analisis Riwayat Waktu
Analisis Spektrum Respon

## Slide 5
Equation of Motion
With
Introducing the modal analysis equation ,
and pre-multiply with [f]T

## Slide 6
Mn
Cn
Kn
Ln
Mn = Generalized Mass
Cn = Generalized Damping
Kn = Generalized Stiffness
Ln = Earthquake Excitation Factor
(1)
Dividing Eq.(1) by Mn, gives :
(2)

## Slide 7
Let
Eq. (2) becomes :
The qn(t) is readily available once Eq.(4) has been solved for Dn(t), utilizing numerical time stepping methods for SDF systems.
(3)
(4)
SDoF

## Slide 8
Response History Analysis
Response Spectrum Analysis
(5)
(6)
(7)
(8)
An(t) = wn2Dn(t)
An= wn2Dn

## Slide 9
BS Response from each mode can be combine using either SRSS
or CQC Method

## Slide 10
Example 1
Determine maximum Base Shear due to El Centro Acc.
Use Respon Spectrum Method
Use SRSS Method to combine BS from each mode
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45

## Slide 11
Mode 1, w1 = 10,76 rad/dt – T1 = 2p/w1 = 0,58 det
Sd1 = 2,5 inch = 6,35 cm
Hitung L1 = {f1}T[M]{1}
M1 = {f1}T[M]{f1}
G1 = L1/M1
{uj} = {f1}G1.Sd1
{fj} = [M]{uj}w12
Mode 2, w2 = 38,28 rad/dt – T2 = 2p/w2 = 0,16 det
Sd2 = 0,18 inch = 0,4572 cm
Hitung L2 = {f2}T[M]{1}
M2 = {f2}T[M]{f1}
G2 = L2/M2
{uj} = {f2}G2.Sd2
{fj} = [M]{uj}w22

## Slide 14
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
19.525,21 kg
6.424,51 kg
19.525,21 kg
28.669,23 kg
BS1 = 25.949,72 kg
BS2 = 9.144,02 kg
BS = ((BS1)2 + (BS2)2)0,5 = 27.513,65 kg
Cara SRSS

## Slide 15
Tugas 8
Determine maximum Base Shear due to El Centro Acc.
Use Respon Spectrum Method
Use SRSS Method to combine BS from each mode
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
W3 = 20.000 kgf
W10x21
W10x21
u3
3 m